## Slide 1
One leg = one smooth loop
Every leg repeats the same cycle: lift and swing forward, then push back
thws
Your Name
1
The swing is a cubic Bézier curve
P0
P1
P2
P3
SWING · foot in the air · 33 %
STANCE · foot on the ground pushes back · 67 %
walking direction →
Why Bézier?
4 control points shape the motion
Starts and stops gently → no jerks for the servos
Shoulder: swings back → front
Knee: lifts the foot, then puts it down
Both joint angles follow this curve · recomputed 50× per second for every leg
Parameters in this loop
these numbers define the curve
shoulder_home
0.687 rad
leg angle when standing
sweep
0.35 rad
how far the leg swings = step length
knee_home
−1.0 rad
knee angle on the ground
knee_lift
−1.3 rad
knee angle in the air = step height
cycle_period
1.4 s
time for one loop = speed
Notes: Every leg repeats one loop. In the swing, about a third of the time, the foot is in the air and moves forward. In the stance, the other two thirds, it is on the ground and pushes back, and that push moves the body forward. The swing follows a cubic Bezier curve: four control points shape the motion, and it starts and stops gently, so the servos get no jerks. Both joint angles, shoulder and knee, follow this curve, 50 times a second. On the right are the numbers that define this loop.

## Slide 2
Four legs in rhythm: walk and trot
All four legs run the same loop, just shifted in time
thws
Your Name
2
When is each foot in the air?
foot in the air (swing)
Walk
one leg at a time
slow · very stable
Front right
Front left
Rear right
Rear left
Trot
diagonal pairs together
faster
Front right
Front left
Rear right
Rear left
0 s
one cycle = 1.4 s
front-right + rear-left ↔ front-left + rear-right
Parameters for timing
only cycle_period is tuned later
cycle_period
1.4 s
time for one loop → smaller = faster
swing share
33 % / 45 %
walk / trot (fixed)
leg offsets
fixed
pattern that makes it a walk or a trot
Notes: All four legs run the same loop, just shifted in time. In a walk only one leg is in the air at a time: slow, but very stable. In a trot, diagonal pairs move together: front-right with rear-left, then front-left with rear-right. That is faster. The speed of the whole thing is set by the cycle period.

## Slide 3
Steering, and the 6 numbers behind it all
Our hips can't move sideways, so we steer like a tank
thws
Your Name
3
Steering = different step lengths left vs right
Turn on the spot
left legs step back
right legs step forward
Walk in a circle
inner legs take shorter steps
outer legs take full steps
The robot measures its own rotation and stops at the exact angle / circle size we ask for
The 6 gait parameters
shoulder_home
0.687 rad
standing leg angle
sweep_left
0.35 rad
step length, left legs
sweep_right
0.35 rad
step length, right legs
knee_home
−1.0 rad
knee on the ground
knee_lift
−1.3 rad
knee in the air = step height
cycle_period
1.4 s
time for one loop = speed
Next: RL tunes these 6 numbers
Notes: Our sideways hip joints are locked, so we steer like a tank. To turn on the spot, the left legs step backward and the right legs forward. To walk in a circle, the inner legs take shorter steps. The robot measures its own rotation and stops at the exact angle or circle size we ask for. Everything you saw is controlled by only six numbers. Different left and right step lengths make it curve. We picked these by hand - are they the best? That is where reinforcement learning comes in.